final	220712 inject Ca curve KCl

Measure Ca dependence with NADPH present from start +KCl
add enzyme to plate, add Ca free NADPH buffers with KCl preincubat 5 min 27
start with NADPH containing Ca stocks (prewarmed to 27 deg, added by 12 well pipet )

Enzyme D1S 180920; pCDH 181030 (see “invitro summary.ods”) and dilution below
Use Gain= 80, lamp low, 20 reads 10 delay temp = 27 deg
read 530ex 590em AR; 340ex 460em NADPH
read 2 h min 2 min intervals

Solutions

1. 1M KCl from 3 M KCL from 220621exp; 1 ml + 2 ml H2O =1 M
2. 20 X HEPES Reaction Buffer 1 ml
4. make 1 x HEPES = 50 ul 20X + 950 ul H2O
5. Dilute NADPH 10 ul + 90 ul of 1X hepes buffer: 10 ul 20X +190 uL H2O
6. made further dilution of NADPH 1:10 in 1X Hepes to 9e-04 M

1. H2O2 std curve
  1. Prepare a 50 µM H2O2 solution from 9.7 M 30% wt/wt stock. H2O2 SIGMA # 1009-100 ml batch MKBG7063 10/4/11 Refrigerator #1 TCR ml (non autoclaved) microcentrifuge tubes
    1. Dilute 30% stock 1:10 H2O = 0.97M	100 uL + 900 uL H2O
    2. Dilute 5 µl with 480 µl H2O to make a 10 mM stock
    3. Dilute the 5 µl into 995 µl of H2O to make 50 µM stock
2. Protocol (Standard Curve):
  1. The total volume per well of this assay is 100 µl. 95 µl each different AR/HRP rxn mix + 5 µl H2O2 std.

[H2O2] µM	[H2O2]	H2O2 (µl)	0.25 M sucrose (µl)	Dil stock µM	[final] µM in assay	[final] nM in assay	nMoles/100 µL assay
50
A	0	0	50		0		0
B	0.05	5	495	0.5	0.025	25	0.0025
C	0.1	10	490	1.0	0.05	50	0.005
D	0.25	25	475	2.5	0.125	125	0.0125
E	0.5	50	450	5.0	0.25	250	0.025
F	1	100	400	10.0	0.5	500	0.05

Comments / Problems:

SUMMARY OF RESULTS:

Order:

1. set up GEN5 exp save
2. 3x 12 well trays
3. prepare H2O2 stds
4. ice
5. thaw Hepes, FAD, thapsi, AR HRP NADPH
6. prepare 20 x HEPES
7. Make 1x HEPES
8. make rxn solutions with HRP NADPH and injection solutions–
9. transfer rxn solutions to 27deg
10. dilute NADPH (both dilutions)
11. add AR to multiwell tray
12. thaw D1S and pCDH
13. dilute enzymes with NADPH +/- KCl and 1x HEPES
14. aliquot H2O2 stds into plate
15. aliquot Enzyme into plate with eppendorf repeater –
16. add STDS mix (D2-Ca) to AR to aliquot 95 per well to row E with repipettor
17. pipette rxns 1 ml of each to 12 well tray with AR
18. pipet 95 ul to assay plate, mix wells with eppendorf multiwell row D to Row
19. read 5 min
20. aliquot injection solutions to 12 well tray
21. pipet 10 ul injection to row E (eppendorf repeater syringe)
22. pipet 10 ul injection to rows A – D with 12 channel pipette to start reactions
23. mix wells with eppendorf multiwell
24. read for 8000 secs (>2h)