HEM18-01-L1 - List of Works requiring Rectification
Revision C - 7 October 2020

Dear Kisiel Group

Lakeside, 82 Eaton Drive, Kingston-upon-Thames, Surrey KT2 7QZ

Under Clause 2.30 of the Contract, please take notice of the list defects requiring rectification.

The list has been divided into five sections: i.e.
1. Balconies
2. External decorations
3. Window seals
4. Triflex parapet repair
5. General

Please provide a Schedule and Method to indicate when and how the defects will be rectified.

If further information is required, please contact the Supervising Officer at the earliest opportunity.

Regards

Daniel Brown (Supervising Officer)
1. Balconies
This is a General List of Rectification that applies to every balcony. There were works specific to individual balconies and when access has been granted to allow the work to be completed, any additional work would be highlighted by the Clerk for the Works.

General Rectifications applying to every balcony
	The pins holding the slats to the wrought-iron have started to rust. The Contract Documents specified non-ferrous pins. / Clean rust-stains from plastic-slats / Replace every pin with a Stainless-steel pin.
	The paint applied to the wrought iron has flaked exposing the wrought-iron. There are areas of old paint that have not been removed or prepared properly and these were beginning to lift and flake. / Sand down all defective areas of handrail, remove flaking paint and sand exposed edge to a smooth secure surface ready to be redecorated.
	The wrought-iron feet that rest onto the concrete panel of the end balconies were rusting. The underside of the feet were not painted which rusted and stained the masonry paint. / Remove rust from all surfaces and prepare ready for decoration. It would be necessary to lift each foot and to apply paint to the underside. The paint must be allowed to dry before lowering the foot.
	Many areas of rust were appearing in the wrought-iron. The rust was found to be very deep in certain areas. / Using a NEEDLE GUN, remove all rust from the wrought iron. This includes the deep areas around the base of the iron balustrades. / With the iron exposed apply a rust inhibitor to prevent further rust.
	Paint has been applied to the mastic line at the base of the concrete-parapets. There are paint marks on the asphalt balcony floor. / Clean down mastic and asphalt and using a bitumen paint, obliterate all white paint on asphalt surfaces. Leave a well-cut paint-line where the white-paint meets the asphalt.