Outer document title
Outer document cover
Table of Contents

# heading 1
If I didn’t want to start a fresh page then I’d want the next section to start here:

Description Of 3 Phase Mains Input Connection

Round connector pinout / Pin 1 Reserved / Pin 2 Reserved / Pin 3 Live Phase 2 / Pin 4 Earth / Pin 5 Live Phase 3 / Pin 6 Live Phase 1 / Pin 7 Neutral / Neutral is mandatory, failure to provide / a neutral will result in damage

According to current documents there is a menu option “Bias control”
The option appears in the RFG setup menu, and is accessable via the RS232 interface.
Currently on the 2069 analogue controller the option is not implemented, the bias control facility is only selectable via the “Remote” analogue interface.

Changes to “Digital Dial Instructions”
Was
Tune and Load display	Select whether load, tune, and bias values should be displayed (OPTION).
Bias control/ Remote FB	Select bias-controlled operation.
Remote ON select	Select automatic/remote control of RF On.

Change to
Tune and Load display	Select whether load, tune, and bias values should be displayed (OPTION).
Bias control/ Remote FB	Unimplemented option
Remote ON select	Select automatic/remote control of RF On.

Changes to RFG remote and RS232
Was
12	Tune and Load display	0=no, 1=show load and tune, 2=also show bias
13	Bias control/ Remote FB	1=on, 0=off
14	Remote ON select	1=on, 0=off

Change to
12	Tune and Load display	0=no, 1=show load and tune, 2=also show bias
13	Bias control/ Remote FB	Unimplemented option
14	Remote ON select	1=on, 0=off

If clarification is needed then the answer would be:
On X2054 and X2069 analog controllers Remote feedback can only be selected from the Remote connector.
The extra menu option was introduced at version 0.84 before the remote panel special, in anticipation of a new controller version designed for menu control.
Removing the option would result in minor changes to the serial control commands.

# Remote Control Operation

A CPS RFG may optionally be controlled by an external device, either an external switch or power dial to allow manual control from another location, or a computer or PLC for full automation.

Remote control operation may be selected from the front panel or hardwired by means of links in the Remote Connector.

The RFG may be operated Manually by fitting the pre-wired plug as supplied.

#### Remote control selection from the front panel
Where the RFG is to be used with partial remote control the remote mode may be selected from the RFG front panel, allowing for manual override when required.
There are two separate remote control options:
Remote On/Off disables the RF On and RF Off controls and instead the RF output turns on in response to an external “ON” signal.
Remote Power Set disables the Power control dial and instead takes the power setting from an external signal.

#### Remote control selection from the Remote connector
In some cases it is desirable to “lock” the RFG into remote control mode, particularly when the RFG is used with automation and operators are not to be allowed to use manual control.
In this case Remote Control may be “Forced” by making one or more “Enable” links in the connector. The links takes priority over the front panel. In this case the front panel switch is overridden and will not return the unit to manual control.

#### Manual operation of the RFG
To return an RFG to manual mode disconnect the remote control cable and fit a minimal Remote plug, either the CPS-supplied plug or a replacement 25 way D plug with a link from pin 13 to 25, then deselect the two remote control functions on the front panel.

#### Computer control and monitoring of RFG (Option)
The interface is implemented as RS232 using two pins of the “remote” connector. The protocol is described in another section.
# Remote Control connector
PAGE 1/5

The 25-way D type connector on the rear panel allows remote control of the generator. Below is a description of the various remote functions.

Pin	Function

1	Remote Setpoint negative	14	RF Off light
2	Remote Setpoint positive.	15	Enable Remote ON
3	Forward power	16	Enable Auxiliary Feedback
4	Reflected power	17	Enable Remote Setpoint
5	Remote RF On	18	-
6	Pulse mode *	19	RF On light
7	Ground	20	+5V out
8	Ground	21	Enable True Power mode
9	Auxiliary feedback negative	22	CEX mode *
10	Auxiliary feedback positive	23	-
11	Serial TXD *	24	-
12	Serial RXD *	25	+12V out for interlock
External interlock
*	Not on all RFG models

(Issue 2.00 02-12-2016)
## Description Of Remote Status Connections / Functions
PAGE 2/5

Pin 3	Incident power. Pin 3 is an analogue output voltage 0-5 volts representing zero to maximum output power.

N.B.	This output can source 5mA.

Pin 4	Reflected power. Pin 4 is an analogue output voltage 0-5 volts representing 0-maximum output power.

N.B.	This output can source 5mA.

Pin 14	RF Off light. Pin 9 is an open collector transistor that grounds with RF Off. This can sink 45mA 20V.

Pin 19	RF On light. Pin 9 is an open-collector transistor that grounds with RF On. This can sink 45mA 20V.

Pin 20	+5V. This is a +5V 500mA Output.

Pin 7,8	Ground

## Description Of Remote Switching and Power control
PAGE 3/5

Remote RF ON	Remote Output set

Pin 5	RF On/Off. To enable this function connect pin 10 to a ground pin. To enable RF connect pin 5 to a ground pin, via a switch, transistor or relay. This is not latching, grounding pin 5 will switch RF On, and removing this ground will switch RF Off.

N.B.	Interlock functions will operate normally when using this function.

Pin 15	Remote RF On/Off Switch Enable. Ground this pin to enable the remote RF On/Off control function, when it is enabled the remote indicator on the front panel is illuminated.

Pins 1,2	Remote power set. To enable this function connect pin 17 to a ground pin. The set point or control is a positive voltage in the range 0v to 5v. 0 volts gives zero output power and 5 volts gives maximum output power.

Pin 17	Remote RF setpoint enable. Ground this pin to enable the remote setpoint control, when it is enabled the remote indicator on the front panel is illuminated.

Pins 7,8	Ground

## Description Of Remote Interlock Connection / Function

PAGE 4/5

Pin 13	External Interlock. When this pin is connected to +12v it allows the generator output to be switched on. When this pin is open-circuit the “External” warning light will illuminate.

Pin 25	Positive supply, +12V or +24V depending on specific RFG model.

Pin 7,8	Ground
## Description Of Auxiliary feedback Connection / Function
PAGE 5/5

Auxiliary feedback is typically used in vacuum processes in order to control the dark space bias potential. The following drawing shows the connections to link the CPS RF generator to a CPS automatic matching network controller.

Pin 9	Auxiliary feedback negative. To enable this function connect pin 16 to a ground pin. The feedback signal should be a negative voltage in the range 0v to –5v. This function is mainly used for plasma dark-space potential (bias) control.

Pin 10	Auxiliary feedback positive. To enable this function connect pin 16 to a ground pin. Connect this pin to ground at the AMN controller

Pin 16	Remote feedback enable. Ground this pin to enable the Pin1 Auxiliary feedback function.

NB.	When using the auxiliary feedback facility, if feedback voltage is not present then RF power will rise to maximum. On plasma systems this is often advantageous as it allows the generator to supply high power to strike plasma, then cut back to operating level as soon as plasma is struck.

## Other functions

Pin 6	Pulse mode. Ground to select pulsed RF operation.

Pin 22	CEX mode. Ground to select CEX (Common exciter or synchronised) operation.

Pin 20	+5V. This is a +5V 500mA Output. This may be used as a power source to illuminate LEDS or power small adapter circuits or displays.

Pin 6	Not Used

Pin 7,8	Ground
# Serial/RS232 Control and Monitoring (Where fitted)
PAGE 5/5

A serial connection may be used to connect the RFG to a computer or other control device. The 25-way connector is NOT directly compatible with a computer serial connector and an adapter lead is required.
The interface has a common ground with the RFG, and in noisy environments an external optical isolator may be added.

Pin 5	RF on/off. In order for RF to be enabled by a serial command this pin must be grounded. If the serial interface will not be used to enable RF then this pin may still be used as a remote input as per page 7 or should be left disconnected.

Pin 11	RFG TXD needs to connect to RXD of a computer or controller

Pin 12	RFG RXD needs to connect to TXD of a computer or controller

Pin 7,8	Ground
## RFG Serial communication Protocol (Where fitted)

The RFG uses MODBUS-RTU, using 9600 baud, 8 bits, one stop bit and no parity. The connection is made via spare pins of the remote connector.

The RFG implements only part of the protocol, specifically the commands for reading and writing of “coils” and “registers”. Coils are used for the On/Off status of the unit, and Registers are used for other parameters as shown in the table further down. There are limits to the number of registers that may be read or written in one operation. Currently the limit is read 12, write 10.
As of version 0.880 it is possible to set a “slave” address, potentially allowing multiple RFGs on one port.
A diagnostic feature will echo single characters back, allowing serial connection to be confirmed without the use of a MODBUS master. This feature is disabled if a device address is set
Command	Function	Notes
1	Read coils	Coils=bits
2	Read inputs	Duplicates “1”
3	Read holding registers	Limit 12 in one operation
4	Read input registers	Duplicates “3”
5	Force single coil
6	Force single register
15	Force multiple coils
16	Force multiple registers	Limit 10 in one operation

The “register” map used is set out at the end of the document. In essence each controllable function is given a number, so a write command consists of a register and a data value. A read command sends a register number and receives a data value.

#### Register map for version 0.880
The following is the register map in use in the 0.880 release of the software. This is based on the layout of the RFG set-up menu.
#### Coil (bit) map:
Bit	Function
0	Cooling Interlock	1=interlock broken, 0=clear
1	External Interlock	1=interlock broken, 0=clear
2	Not Used
3	Spare/Rear panel Interlock	1=interlock broken, 0=clear
4	Not Used
5	Not Used
6	Timer ended	1=timer run out
7	Cool-down period	1=cool down in progress
8	Not Used	Writable
9	Not Used	Writable
10	Not Used	Writable
11	Not Used	Writable
12	Remote RF Off	Writable, 1 sets RF Off, self-clearing
13	Remote RF On *	Writeable, 1 sets RF On, self-clearing
14	RF Off light/Ready	1=on, 0=off
15	RF On light/RF is ON	1=on, 0=off

*Important: Remote RF On works by pulsing the Remote On/Off function so a link is needed on the remote connector, pin 5 to ground (pin 7) to enable Computer control of RF On. Conversely if the link is omitted then RF can only be enabled manually or by a remote contact-closure.
#### Register (16 bit word) map for version 0.883
Note that the map closely matches the RFG’s menu options. As a result some registers are of little interest but are still accessible e.g. registers 12, 21 and 29.
Register	Function
0	Version number	Example 883 for ver. 0.883
1	Offset to forward power reading	4
2
3	“Coil” map as a number	16 bit value
4	Forward power	Value (Read-only)
5	Reflected Power	Value (Read-only)
6	Timer select	1=on, 0=off
7	Time Set	0-100
8	Time Range	0=seconds, 1=minutes
9	Cool-down	1=on, 0=off
10	Power Set	0-1000
11	Ramp	0-200 in tenths of a second
12	Tune and Load display	0=no, 1=show load and tune, 2=also show bias
13	Bias control/ Remote FB	Not implemented see below
14	Remote ON select	1=on, 0=off
15	Remote SET select	1=on, 0=off
16	Divide 10 select	1=on, 0=off
17	CEX input select	1=on, 0=off
18	Pulse select	1=on, 0=off
19	Pulse Frequency Select	0=External, 1=500Hz,2=1kHz, / 3=2kHz, 4=5kHz, 5=10kHz
20	Pulse Duty %	0-100 (10us minimum)
21	Key Lock	1=on, 0=off
22	Dial Lock	1=on, 0=off
23	Device Address	0-255 (0=Ignore address)
24	Display brightness	0-3, no immediate effect
25	Tune	Value
26	Load	Value
27	Bias	Value
28	Freq Trim	Reserved for future expansion
29	Freq Offs	Reserved for future expansion
30	Freq Fix	1=inhibit auto-tuning
31	Trim Step	0=1,1=10,2=100 (ignore)
32	Alarm Out	0=None 1=En_Rem_On 2=En_Rem_Set / 3=Both Rem pins
33	User Pass (Unimplemented)	Ignored
34	Show pass	0=Hide (use stars), 1=show

Bias control function is not software selectable, if required it must be enabled using the remote connector link.
Pulse Generation is an option and may not be equipped on all RFGs. On an unequipped unit the setting will always revert to 0 (External).
## Register map for version 0.876
The map for 0.876 is mostly identical to 0.870 (see below) except for the addition of the “Alarm Out” option.

0	Version Number	876 (for version 0.876)
22	Load	Value
23	Bias	Value
24	Alarm Out	0=None 1=En_Rem_On 2=En_Rem_Set / 3=Both Rem pins
25	User Pass (Unimplemented)	Ignored
26	Show pass	0=Hide (use stars), 1=show

#### Register map for version 0.870-0.875
The following is the register map in use in the 0.870 release of the software.
Minor updates to 0.875 still “identify” as 0.870 via serial as the map has not changed.
 This is based on the layout of the RFG set-up menu.
The Coil (bit) map is the same as for version 0.883
Bit	Function
0	Cooling Interlock	1=interlock broken, 0=clear
1	External Interlock	1=interlock broken, 0=clear
2	Not Used
3	Spare/Rear panel Interlock	1=interlock broken, 0=clear
4	Not Used
5	Not Used
6	Timer ended	1=timer run out
7	Cool-down period	1=cool down in progress
8	Not Used	Writable
9	Not Used	Writable
10	Not Used	Writable
11	Not Used	Writable
12	Remote RF Off	Writable, 1 sets RF Off, self-clearing
13	Remote RF On *	Writeable, 1 sets RF On, self-clearing
14	RF Off light/Ready	1=on, 0=off
15	RF On light/RF is ON	1=on, 0=off

*Important: Remote RF On works by pulsing the Remote On/Off function so a link is needed on the remote connector, pin 5 to ground (pin 7) to enable Computer control of RF On. Conversely if the link is omitted then RF can only be enabled manually or by a remote contact-closure.
#### Register (16 bit word) map for version 0.870
Note that the map closely matches the RFG’s menu options. As a result some registers are of little interest but are still accessible e.g. registers 12, 21 and 26.
Register	Function
0	Version number	Example 870 for ver. 0.870
1	Offset to forward power reading	4
2
3	“Coil” map as a number	16 bit value
4	Forward power	Value (Read-only)
5	Reflected Power	Value (Read-only)
6	Timer select	1=on, 0=off
7	Time Set	0-100
8	Time Range	0=seconds, 1=minutes
9	Cool-down	1=on, 0=off
10	Power Set	0-1000
11	Ramp	0-200 in tenths of a second
12	Tune and Load display	0=no, 1=show load and tune, 2=also show bias
13	Bias control/ Remote FB	Not implemented see below
14	Remote ON select	1=on, 0=off
15	Remote SET select	1=on, 0=off
16	Divide 10 select	1=on, 0=off
17	CEX input select	1=on, 0=off
18	Pulse select	1=on, 0=off
19	Key Lock	1=on, 0=off
20	Dial Lock	1=on, 0=off
21	Display brightness	0-3, no immediate effect
22	Tune	Value
23	Load	Value
24	Bias	Value
25	User Pass (Unimplemented)	Ignored
26	Show pass	0=Hide (use stars), 1=show

Bias control function is not software selectable, if required it must be enabled using the remote connector link.

### Hello

# Hello