According to current documents there is a menu option “Bias control”
The option appears in the RFG setup menu, and is accessable via the RS232 interface.
Currently on the 2069 analogue controller the option is not implemented, the bias control facility is only selectable via the “Remote” analogue interface.

Changes to “Digital Dial Instructions”
Was
Tune and Load display	Select whether load, tune, and bias values should be displayed (OPTION).
Bias control/ Remote FB	Select bias-controlled operation.
Remote ON select	Select automatic/remote control of RF On.

Change to
Tune and Load display	Select whether load, tune, and bias values should be displayed (OPTION).
Bias control/ Remote FB	Unimplemented option
Remote ON select	Select automatic/remote control of RF On.

Changes to RFG remote and RS232
Was
12	Tune and Load display	0=no, 1=show load and tune, 2=also show bias
13	Bias control/ Remote FB	1=on, 0=off
14	Remote ON select	1=on, 0=off

Change to
12	Tune and Load display	0=no, 1=show load and tune, 2=also show bias
13	Bias control/ Remote FB	Unimplemented option
14	Remote ON select	1=on, 0=off

If clarification is needed then the answer would be:
On X2054 and X2069 analog controllers Remote feedback can only be selected from the Remote connector.
The extra menu option was introduced at version 0.84 before the remote panel special, in anticipation of a new controller version designed for menu control.
Removing the option would result in minor changes to the serial control commands.