# Appendix A: Linear Algebra

## Bases of a vector space
The aim of this short introduction to Linear Algebra is to explain the nullspace concept and method in the solution of linear homogeneous equations. The method has been used in Chapter 2 for balancing the stoichiometric coefficients of chemical reactions. A more general treatment addressing spacecraft dynamics and control can be found in [1].
### Vectors, matrices and bases
Linear algebra extends 3D vector properties and operations to a generic vector space V , which is here assumed real and finite dimensional for simplicity. In this case, V=R^n where n is the space dimension, and a generic vector bold v (in bold font) is an n-ple of real numbers, which can be written either in column form or by using the inline convention [1], as follows
bold v=[ v_1,...,v_k,...v_n ]," " v=left[ stack{v_1 # ... # v_n} right] .	(11.1)

A vector space has the property that the sum of two vectors bold v_1+ bold v_2 in V belong to the space itself and the product %alpha bold v in V of a vector by a real scalar %alpha , too.
When n=3 , the vector bold v can be interpreted as the coordinate vector bold v=[ v_1,v_2,v_3 ] of the oriented segment from the origin O of a Cartesian frame to a generic point P , denoted by vec v = vec OP .
m vectors of R^n can be collected into the columns of a matrix V, n times m , as follows:
V=left [ matrix{bold v_1 # ...# v_j# ... # bold v_m } right ]=left[ matrix{ v_11 # ...# v_1j # ...# v_1m ## " " # ...# " "#" "# " " ## v_i1 # ... # v_ij # ...# v_im ## " " # " "# " "# ...# " " ## v_n1 # ... #v_nj # ...# v_nm} right ] .	(11.2)

One may ask if it is possible to represent a generic vector as a linear combination of the matrix vectors, like
bold v=x_1 bold v_1 + ... +x_k bold v_k + ...+x_m bold v_m=V bold x .	(11.3)

This is always possible, but in general the vector bold x in R^m is not unique. The coefficients x_k are the coordinates of bold v with respect to the matrix V . The geometric meaning is that m vectors of V generate a subspace S( V ) in R^n , which is the generalization of a plane passing through the origin in the 3D space. An important question is the dimension %mu of this subspace, since in the case of %mu=m , the representation in (11.3) becomes unique. In other terms, a unique vector bold x in R^m exists which premultiplied by V generates bold v . One say that the subspace S( V ) is spanned by the columns of V , and the columns become a vector basis of the subspace.
Which is the condition for the m vectors of V to span a subspace of dimension m ? They must be linearly independent, in other terms, no vector bold v_k of V can be represented as a linear combination of the other vectors. Formally, we the inequality
bold v_1 <> x_2bold v_2 + ...+x_k bold v_k + ...+x_m bold v_m	(11.4)

holds, whichever be the m-1 coefficients. The geometric meaning is that each vector does not lie in the subspace spanned by the remaining vectors. In the 3D case, any of the three Cartesian axes lbrace widevec {i} _1 , widevec {i} _2, widevec {i} _3 rbrace cannot be written in terms of the other two. Figure 11.1 shows three vectors widevec {v} _1, widevec {v} _2, widevec {v} _3 lying in the xy plane, which therefore cannot be LI. In fact, only a pair of them is LI, and a pair of them plus widevec {v} _4 , which does not lie in the xy plane, are LI in the 3D space, which is spanned by them.
Up to now m is generic. We consider three specific cases:

Figure 11.1 Vectors in a 3D space.
1) m=n : if the n vectors bold v_k," " k=1,...,n are linearly independent, they become a basis for the whole vector space R^n , like the Cartesian axes for R^3 .
2) m>n : the m vectors cannot be linearly independent, like the three Cartesian axes of R^3 and a fourth vector, which can be written as a linear combination of the three axes. Let us remark, that also in the case m>n , the number of linear independent vectors may be less than n, in which case they cannot span the whole vector space R^n .
3) m<n: if the m vectors are linearly independent, they generate and span a subspace of dimension m, like the x and y axes span the xy plane of dimension 2 orthogonal to the z axis in Figure 11.1.
## References
E. Canuto, C. Novara, L. Massotti, D. Carlucci and C. Perez Montenegro, Spacecraft Dynamics and Control: the Embedded Model Control Approach, Butterworth-Heinemann, 2018, Oxford, UK.